## Slide 1
4-Bit Binary-to-Decimal
Conversion and Display System
Design • Logic • Simulation • 7-Segment Display
1

## Slide 2
Project Objective
What the system is designed to do
Input
Accept a 4-bit binary number using four switches: B3 B2 B1 B0 Range: 0000 to 1111
Conversion
Convert the 4-bit binary value into decimal digits. 0–9 → one digit 10–15 → two digits
Output
Show the decimal value using two 7-segment displays. Example: 1011 → 11
2

## Slide 3
System Architecture
Simple block diagram of the complete system
4-Bit Input
B3 B2 B1 B0
Binary → BCD
Conversion logic
BCD → 7-Segment
Display drivers
Decimal Display
Tens + Ones
3

## Slide 4
4-Bit Binary Input
Each switch represents one binary bit
B3 | B2 | B1 | B0 | Decimal
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 1 | 0 | 0 | 4
1 | 0 | 0 | 0 | 8
1 | 1 | 1 | 1 | 15
Formula: Decimal = B3×8 + B2×4 + B1×2 + B0×1
4

## Slide 5
Binary-to-BCD Conversion
The important step for displaying 10–15
For 0 to 9
0000 to 1001 The value can be displayed as a single decimal digit. Example: 1001₂ = 9₁₀
For 10 to 15
1010 to 1111 The value is split into: • Tens digit = 1 • Ones digit = 0 to 5 Example: 1111₂ = 15₁₀
5

## Slide 6
Truth Table
All possible 4-bit inputs and decimal outputs
Binary | Decimal | Tens | Ones
0000 | 0 | 0 | 0
0001 | 1 | 0 | 1
0010 | 2 | 0 | 2
0011 | 3 | 0 | 3
0100 | 4 | 0 | 4
0101 | 5 | 0 | 5
0110 | 6 | 0 | 6
0111 | 7 | 0 | 7
1000 | 8 | 0 | 8
1001 | 9 | 0 | 9
1010 | 10 | 1 | 0
1011 | 11 | 1 | 1
1100 | 12 | 1 | 2
1101 | 13 | 1 | 3
1110 | 14 | 1 | 4
1111 | 15 | 1 | 5
6

## Slide 7
Logic and Display Stage
How the converted digits reach the 7-segment displays
• Use combinational logic or a binary-to-BCD converter block.
• Feed the BCD tens digit and BCD ones digit to display decoders.
• 7446/7447-type BCD-to-7-segment decoders can be used in hardware implementations.
• Each 7-segment display shows one decimal digit.
• Use current-limiting resistors (typically 220 Ω or 330 Ω) for LED segments in hardware.
7

## Slide 8
Logisim-Evolution Simulation
Recommended for a simple first-year digital-logic project
1. Inputs
Place four input switches. Label them B3, B2, B1, B0. Set each switch to 0 or 1.
2. Logic
Build the conversion section using logic gates / suitable converter blocks. Test each binary input.
3. Display
Connect BCD outputs to 7-segment display blocks. Check that 0000–1111 gives 00–15.
8

## Slide 9
Example Simulation
One input, one conversion, one display result
Input
B3 B2 B1 B0 1 0 1 1
Conversion
1011₂ = 11₁₀ BCD = 0001 0001
Display
Tens = 1 Ones = 1 Display: 11
9

## Slide 10
Verification and Testing
Check every possible input
• Toggle the four input switches through all values from 0000 to 1111.
• Confirm 0000 to 1001 display 0 to 9 correctly.
• Confirm 1010 to 1111 display 10 to 15 correctly.
• Check that the tens display changes from 0 to 1 at decimal 10.
• Record a few test cases as evidence of successful simulation.
10

## Slide 11
Advantages and Applications
Why this small circuit is useful
Advantages
• Simple digital-system example • Demonstrates binary representation • Uses combinational logic • Connects logic to a visual output • Easy to test in Logisim-Evolution
Applications
• Digital counters • Embedded displays • Measurement systems • Digital control panels • Learning and simulation of digital circuits
11

## Slide 12
Thank You
Questions?
12